## Slide 1: Fatigue Crack Growth & Testing Committee – Monthly Meeting
Kevin Walker, committee lead kwalker999@hotmail.com
Robert Pilarczyk, committee co-lead rtpilarczyk@hill-engineering.com
Working Group on Engineered Residual Stress Implementation

## Slide 2: Interference Fit Fastener (IFF) Effort
Overview
  Open literature documents fatigue life benefits due to neat fit and IFF, but there are no well-established and validated methods to account for the benefits
  IFFs are complex due to the combination of applied stress due to interference, applied remote load, and residual stress (e.g., in a cold expanded hole)
  The accuracy of stress intensity factors and crack growth predictions for IFF is highly dependent on the accuracy of the stress analysis
  An initial step for the IFF Working Group (Phase I) involves a series of round-robin stress analysis cases based upon a planned set of experiments
    Opportunity to evaluate differences in process simulation techniques against a set of planned experiments
Objective
  Collaborate to establish validated analytical methods for IFF applications
Approach
  Phased approach with increasing complexity
    Phase I, group 1: Baseline stress analysis
      Open hole (no fastener)
      Model applied loading and unloading (4 stress levels)
    Phase I, group 2: Stress analysis in as-installed state
      Model the fastener install and fastener removal (3 levels of interference)
      Investigate strain and stress field due to fastener installation
      Experimental tests in planning (strain measurements at surface – DIC, strain gages)
    Phase I, group 3: Stress analysis with interference + applied loading
      Model fastener installation, remote loading (4 stress levels), unloading, and fastener removal
      Experimental tests for each step in planning (strain measurements at surface – DIC, strain gages)
  All testing to be performed by SwRI sponsored by A-10 team

## Slide 3: Interference Fit Fastener (IFF) Effort
Current Status
  Phase I, group 1 analysis challenge released in November
    Open hole stress prediction, no fastener
  Test plan in work
Timeline
  Phase I, Group 1 results due Dec 31, 2022
    5 submissions received as of 1/10/2023
    Still waiting for a few submissions
    Results comparisons in next few weeks