## Slide 1: Fatigue Crack Growth & Testing Committee – Monthly Meeting
Kevin Walker, committee lead kwalker999@hotmail.com
Robert Pilarczyk, committee co-lead rtpilarczyk@hill-engineering.com
Working Group on Engineered Residual Stress Implementation

## Slide 2: Interference Fit Fastener (IFF) Effort
Overview
  Open literature documents fatigue life benefits due to neat fit and IFF, but there are no well-established and validated methods to account for the benefits
  A-10 Damage Tolerance Analyses (DTAs) currently do not include any such benefit
Objective
  Develop an empirically validated analytical methodology to quantify the damage tolerance impacts of applicable A-10 fastener installations with neat or interference fits
Approach
  Phased approach with increasing complexity
  Phase 1: assessment of as-installed state
    Simulate and empirically quantify the strain and stress state near a hole in the presence of an interference fit fastener
      3 levels of interference
      3D nonlinear FE process modeling; DIC and strain gages for surface strain measurements
  Phase 2: fastener installed + remote loading
    Repeat Phase 1 but with the addition of remote loading and unloading (multiple load levels and interference levels)
  Phase 3: analytical methodology to account for interference fit fasteners during crack growth
    Perform multi-point fatigue crack growth analyses including interference fit fastener conditions
    Blind predictions prior to fatigue testing to be performed in Phase 4
  Phase 4: fatigue crack growth testing with interference fit fasteners
    Perform fatigue crack growth testing of neat fit and interference fit conditions
    Use fatigue test data for validation and refinement of analytical methodology

## Slide 3: Interference Fit Fastener (IFF) Effort
Current Status
  Test plan in progress
    Currently working on material procurement, coupon manufacturing
Timeline
  Coupon manufacturing expected to finish by xxx
  Phase 1 testing to be performed by xxx